## Slide 1
SPIRAL MIXER
User Manual
USER MANUAL
Warning: Please read the user manual carefully before operating the machine

## Slide 2
1/ The machine must be installed in dry, drafty and bright environmental condition.
2/ Please position the machine on a flat and firm place; you can put it on a workbench whose height fits you, and leave a space around it of 50 cm for easier usage and cleaning.
3/ The machine is constructed to have IPX23 protection level.
4/ The electric network must be provided with an automatic differential switch having characteristics suitable to those of the machine, in which the opening distance between the contacts must be of at least 3 mm. Most of all it is necessary a good ground system. Verify that the electrical set-up corresponds with the numbers of the specification (7) found and on the small label at the back of the machine.
5/ The connections type Y of the machine with the electric network is made by means of an operation cable, which is provided with a plug only in the single-phase model. As far as the three-phase machines are concerned it is necessary to put together the cable and a normalized and polarized plug.
6/ The plug must be easily accessible, must not require any kind of movement. The cable from the machine to the wail plug must not be pulled tightly, also do not rest the machine on the cable.
The machines are provided with the following operation and safety devices：
1/ Operating devices
1.1 / Sing-phase or Three-phase machines (LFM10 model):
a. Green button: Operating (Pict.1)
b. Red button: Stop
1.2/ Sing-phase or Three-phase machines (the rest of the models): ( Pict. 2 & Pict.3 )
B. Main switch
C. Red button: Emergency stop
D. Green button: Operating
E. Timer
Installation
Switch
Pict.2
Pict.1
Pict.3 (2 speed)
1/ Keep in order your working area. Disorder can cause dangerous accidents.
2/ Consider environmental conditions. Do not use the machine in humid, wet or badly lit environments, close to inflammable liquids or gas.
3/ Make sure water and heat sources are at safe distance.
4/ Keep away form children and non authorized personnel.
5/ Only utilize the machine with the correct voltage.
6/ Dress in adequate way. Do not wear hanging clothes or any items that can be caught in the machine. Use no-slip shoes. For hygiene and safety keep your hair tied back and wear protective gloves.
7/ Protect the cable. Do not pull the cable to extract the plug. Do not leave the cable near high temperatures, sharp objects, water or solvents.
8/ Avoid insecure positions. Find the best surface to ensure the machine is balanced.
9/ Take the plug out when the machine is not in use, before cleaning, maintenance and moving it.
10/ Do not use further extensions.
11/ Check that the machine is not damaged. Before using the machine carefully check that all security devices are working. Check that: the mobile parts are not blocked, there are not any parts damaged, all the parts have been set up correctly and all the conditions that could influence the regular functioning of the machine are in working order.
12/ Installing or repairing the machine by qualified personnel. Qualified people, using original spare parts, can only do the installation or repair. The non-compliance with these rules can represent danger for the user.
Warning

## Slide 3
1/ the safety devices G, H, I, J can be installed only in the machines with raising top and removable bowl (LR series).
2/ The safety devices are applicable when:
- Raising the safety guard F (pict.4). The machine stops
- Raising the head (by means of the check pin H and/or taking off bowl the machine does not start)
H
F
J
J
F
H
Pict.4
Pict.6
Pict.5
Safety guard (Pict.4)
Micro-switch(Auto-stop when the guard is up)
Check pin of the head
Locking disk of the bowl.
Before operating the machine, the safety guard F must be completely lowered (pict.6), and the bowl is correctly inserted and locked by the disk J and that the head is down and locked by the check pin H (this must be completely inserted).
After inserting the plug the machine is ready for use.
Safety Device
Working test
Machine mod. LFM10:
Operating: Push the green button a to start the bowl and the spiral (Pict.1)
Stop: Push the red button b.
1/ The rest of the machines models:
Operating: rotate the main switch B in position 1 (Pict.2 ),(the -2V models can rotate 1 or 2)( Pict.3), set timer E and push the Green button D to start the bowl and the hook.
Stop: Rotate the main switch B in the position 0, or push the red button C to stop the bowl and the hook.
In order to operate the machine again after the stop due to the raising of the safety guard F or to the activating of the emergency button C it is necessary to proceed as follows: lower again and completely the safety guard F; release the button C by rotating it clockwise, as shown by the arrow, and push the operating button a or D.
Note
2/ For 3 phase machine, if the rotation of the bowl is opposite to that shown by the arrow, it is necessary to follow these indications for the connection:
Stop the machine
Take the 2 phase wire out
Reverse the wire connection position of two phases (example: L1 with L2 and vice versa)
Restart the machine and verify if the bowl is rotation the right direction.
Start the machine without loading, let it run for about one minute and verify that it is functioning perfectly.

## Slide 4
1/ After lifted up the safety guard F, pour ingredients to the bowl, close the safety guard, and press the operating switch a or D, with timer setting.
2/ The movement made by the hook, which is synchronized with the rotation of the bowl, gives an amalgamation of flour, water, salt, yeast and other eventual ingredients till you obtain a mixture of the consistence required.
3/ If necessary, in order to modify the characteristics and/or the consistence of the initial dough, pour the ingredients through the safety guard F.
4/ When work cycle is completed, leave the machine on hold, lift up the safety guard F to maximum opening, take the mixture out, proceed with cleaning of the machine following the indication at 5.1.
5/ Note: For the LR series, please stop the machine, unplug the machine, raise the safety guard F completely, pull the pin H as far as the head is un-lock, and raise the head by means of the little piston underneath. Then rotate clockwise the disk J as far as the bowl is unlocked, raise the bowl and take it out of the machine. Finally take off the dough.
6/ After cleaning, put the bowl back on, and make sure that the four pins underneath (pict.7) are correctly fixed in the four holes M of the machine; then lock the bowl rotating clockwise the disk J. Put the head down pushing it downwards as far as it is blocked by the pin H.
7/ Usage of the machine provided with timer
The timer is an electromechanical device that allows to program from 1 to 30 minutes
- The work-time of the machine by rotating the knob 0 in the desired position.
- Operate the machine following the instructions of 4.4.
- Once the set time is over, the timer stops the machine.
Important
Before taking off the dough, make sure the timer are in position “0”.
Usage of the machine
Pict.7

## Slide 5
Warning:
1/ Before effecting any kind of maintenance or cleaning, you must cut off the power supply.
In any case of malfunctioning or damage of the machine, you must apply for authorized assistance from the manufacturer or dealer.
2/ The cleaning must be done every time the machine has been used following all the rules to prevent malfunctioning of the machine and for hygienic purposes.
Using a wooden or plastic palate first clean the residue of dough, then with a soft sponge and warm water accurately clean the bowl, the hook, the leading shaft and the safety guard, dry with kitchen paper.
Warning
3/ We recommend not to use any kind of chemical product abrasive or corrosive. Absolutely avoid using spraying water, sharp tools, rough or abrasive objects, metal/sponges etc., which can damage the surfaces and be dangerous from an hygienic point of view.
To maintain the efficiency and security of the machine it is necessary to proceed with periodical maintenance (every 6 months) of the following indications:
4/ Tensioning of the upper chain
The chain must be tensioned it, by checking it, it becomes loose or if the rotation of the hook is not constant: Unscrew the cover P, (Pict.9) loosen the screws Q, Pull the support of the hook R as far as the tension the chain is optimized. Lock the support R with the screws Q, Put the cover P on once more and fix it.
5/ Lubricating the chains
After unscrewing the fixing screws, take away the cover P and the back panels V, put reasonable amount of proper grease on the chains S &T (pict.8-9) , sufficient to lubricate all the links of the chain. Once this is done, mount the two panels and secure again with screws.
Maintenance
Pict.8
Pict.9

## Slide 6
Specification Table
Slephase & single speeding
Electrical diagram
SS: Micro Switch
M: Motor SP: Sensor
QS: Main Switch
T: Transformer
KM: Contactor
PT: Timer
SB1: Start Button
SB2: Stop Button
Power Source Wire:L(red) N(blue)
Ground Wire E:(yellow-green)
Model | HRM-20 | HRM-25 | HRM-30 | HRM-50 | HRM-60
Voltage(V) | 230 | 230 | 230 | 230 | 230
Cycle(Hz) | 50 | 50 | 50 | 50 | 50
Power(KW) | 1.5 | 1.5 | 1.5 | 1.5 | 1.5
Max Dough capacity(KG) | 10 | 16 | 20 | 30 | 35
Hook speed(rpm) | 98 | 98 | 98 | 98 | 98
Bowl speed(rpm) | 10 | 10 | 10 | 10 | 10
Dimension(mm) | 677x353x637 | 720x400x620 | 798x433x726 | 820x485x726 | 880x550x720

## Slide 7
illustration diagram
Item | Description | Qty | Part no. |  | Remark
 |  |  | HRM-20 | HRM-25 | 
1 | Safety guard | 1 | 17-003 | 22-005 | 
2 | Bowl | 1 | 17-002 | 22-006 | 
3 | Bowl Flange | 1 | 22-022 | 22-022 | 
4 | Locking Flange | 1 | 17-005 | 22-008 | 
5 | Transit ring | 3 | 22-053 | 22-053 | 
6 | Bearing 6205 | 5 | 22-055 | 22-055 | 
7 | Bearing support | 1 | 22-019 | 22-019 | 
8 | Chain 126 | 1 | 22-041 | 22-041 | 
9 | Chain wheel 72 | 1 | 22-042 | 22-042 | 
10 | Support axle | 1 | 22-015 | 22-015 | 
12 | Guard ring | 2 | 22-035 | 22-035 | 
13 | Guard axle | 1 | 22-012 | 22-012 | 
14 | Off-set ring | 1 | 22-028 | 22-028 | 
19 | Chain wheel 15 | 1 | 22-043 | 22-043 | 
20 | Spiral support | 1 | 22-020 | 22-020 | 
22 | Bearing 6205 | 1 | 22-055 | 22-055 | 
illustration Part list

## Slide 8
Item | Description | Qty | Part no. |  | Remark
 |  |  | HRM-20 | HRM-25 | 
24 | Mixing Axle | 1 | 22-018 | 22-018 | 
25 | Spiral | 1 | 17-001 | 22-004 | 
27 | Cable fixer | 1 | 22-110 | 22-110 | 
28 | Cable | 1 | 22-082/171/086 | 22-082/171/086 | LRM
 |  |  | 22-125 | 22-125 | LR
 |  |  | 22-098 | 22-098 | LR-2V
33 | Divider | 1 | 22-003 | 22-003 | 
35 | Locker | 1 | 22-048 | 22-048 | 
36 | Lock axle | 1 | 22-014 | 22-014 | 
37 | lock spring | 1 | 22-049 | 22-049 | 
39 | Side cover | 2 | 22-011 | 22-011 | 
40 | Structure | 1 | 22-001 | 22-001 | 
41 | foot | 4 | 22-033 | 22-033 | 
42 | Rubber shoe | 4 | 22-034 | 22-034 | 
43 | Wheel with stopper | 2 | 22-031 | 22-031 | 
44 | Motor | 1 | 22-152 | 22-152 | LRM
 |  |  | 22-046 | 22-046 | LR
 |  |  | 22-153 | 22-153 | LR-2V
45 | Top cover | 1 | 22-009 | 22-009 | 
46 | Head | 1 | 22-002 | 22-002 | 
47 | Nylon ring | 2 | 22-029 | 22-029 | 
49 | Air spring | 1 | 22-051 | 22-051 | 
50 | Micro switch | 1 | 22-079 | 22-079 | 
51 | Head axle | 1 | 22-013 | 22-013 | 
52 | Nylon cover | 2 | 22-030 | 22-030 | 
53 | Electrical box | 1 | 22-096 | 22-096 | 
54 | Wheel | 2 | 22-032 | 22-032 | 
55 | Contactor | 1 | 22-155 | 22-155 | LRM
 |  |  | 22-108 | 22-108 | LR
 |  |  | 22-108 | 22-108 | LR-2V
57 | Emergency stop | 1 | 22-099 | 22-099 | 
58 | Transit ring | 1 | 22-093 | 22-093 | 
61 | Gear box | 1 | 22-074 | 22-074 | 
63 | Back cover | 1 | 22-010 | 22-010 | 
64 | Transformer | 1 | 22-154 | 22-154 | LRM
 |  |  | 22-107 | 22-107 | LR
 |  |  | 22-107 | 22-107 | LR-2V
illustration Part list
Continue………

## Slide 9
Item | Description | Qty | Part no. |  | Remark
 |  |  | HRM-20 | HRM-25 | 
65 | Main Switch | 1 | 22-156 | 22-156 | LRM
 |  |  | 22-169 | 22-169 | LR
 |  |  | 22-157 | 22-157 | LR-2V
66 | Electrical panel | 1 | 22-097 | 22-097 | 
67 | Start Switch | 1 | 22-100 | 22-100 | 
68 | Timer | 1 | 22-103 | 22-103 | 
69 | Chain | 1 | 22-040 | 22-056 | 
70 | Chain wheel 29 | 1 | 22-045 | 22-045 | 
71 | Bearing Connector | 1 | 22-021 | 22-021 | 
75 | Connector axle | 1 | 22-017 | 22-017 | 
77 | Connector key | 1 | 22-024 | 22-024 | 
78 | Engager | 1 | 22-026 | 22-026 | 
80 | Round bearing support | 1 | 22-054 | 22-054 | 
81 | Wheel 14 | 1 | 22-044 | 22-044 | 
83 | Transmission axles | 1 | 22-016 | 22-016 | 
98 | Lever | 1 | 22-172 | 22-172 | 
100 | Hook divider | 1 | 22-185 | 22-185 | 
101 | Hook | 1 | 22-161 | 22-161 | 
103 | Water shield | 1 | 22-187 | 22-187 | 
104 | Adjusting screw | 1 | 22-192 | 22-192 | 
105 | Auxiliary relay PCB | 1 | 22-281 | 22-281 | 
106 | Hook washer |  | 22-193 | 22-193 | 
110 | Electrical complete | 1 | 110-LRM | 110-LRM | LRM
 |  |  | 110-LR | 110-LR | LR
 |  |  | 110-LR-2V | 110-LR-2V | LR-2V
111 | Spiral support complete | 1 | 111-TR17/22 | 111-TR17/22 | 
JR serial illustration Part list
Continue………

## Slide 10
illustration Part list
Item | Description | Qty | Part no. |  |  | Remark
 |  |  | HRM-30 | HRM-50 | HRM-60 | 
1 | Safety guard | 1 | 33-005 | 42-003 | 53-002 | 
2 | Bowl | 1 | 33-006 | 42-002 | 53-001 | 
3 | Bowl Flange | 1 | 22-022 | 22-022 | 22-022 | 
4 | Locking Flange | 1 | 33-008 | 42-005 | 53-004 | 
5 | Transit ring | 3 | 22-053 | 22-053 | 22-053 | 
6 | Bearing 6205 | 5 | 22-055 | 22-055 | 22-055 | 
7 | Bearing support | 1 | 22-019 | 22-019 | 22-019 | 
8 | Chain 144 | 1 | 33-027 | 33-027 | 33-027 | 
9 | Chain wheel 85 | 1 | 33-029 | 33-029 | 33-029 | 
10 | Support axle | 1 | 22-015 | 22-015 | 22-015 | 
11 | Screw | 4 | 22-062 | 22-062 | 22-062 | 
12 | Guard ring | 2 | 22-035 | 22-035 | 22-035 | 
13 | Guard axle | 1 | 33-012 | 33-012 | 33-012 | 
14 | Off-set ring | 1 | 22-028 | 22-028 | 22-028 | 
19 | Chain wheel 15 | 1 | 33-031 | 33-031 | 33-031 | 
20 | Spiral support | 1 | 33-018 | 33-018 | 33-018 | 
22 | Bearing 6205 | 1 | 33-036 | 33-036 | 33-036 | 
24 | Mixing Axle | 1 | 33-017 | 33-017 | 33-017 | 
25 | Spiral | 1 | 33-004 | 33-004 | 33-004 | 
27 | Cable fixer | 1 | 22-110 | 22-110 | 22-110 | 
33 | Divider | 1 | 33-003 | 42-001 | 53-006 | 
35 | Locker | 1 | 22-048 | 22-048 | 22-048 | 
36 | Lock axle | 1 | 33-014 | 33-014 | 33-014 | 
37 | lock spring | 1 | 22-049 | 22-049 | 22-049 | 
39 | Side cover | 2 | 33-011 | 42-008 | 53-007 | 
41 | foot | 4 | 33-024 | 33-024 | 33-024 | 
42 | Rubber shoe | 4 | 22-034 | 22-034 | 22-034 | 
43 | Wheel with stopper | 2 | 33-022 | 33-022 | 33-022 | 
44 | Motor | 1 | 33-048 | 42-006 | 42-006 | LRM
 |  |  | 33-033 | 33-033 | 33-033 | LR
 |  |  | 33-049 | 33-049 | 33-049 | LR-2V
45 | Top cover | 1 | 33-009 | 33-009 | 33-009 | 
47 | Nylon ring | 3 | 22-029 | 22-029 | 22-029 | 
49 | Air spring | 1 | 22-051 | 22-051 | 22-051 | 
50 | Micro switch | 1 | 22-079 | 22-079 | 22-079 | 
51 | Head axle | 1 | 33-013 | 33-013 | 33-013 | 
52 | Nylon cover | 2 | 22-030 | 22-030 | 22-030 | 
53 | Electrical box | 1 | 22-096 | 22-096 | 22-096 | 
54 | Wheel | 2 | 33-023 | 33-023 | 33-023 | 
55 | Contactor | 1 | 22-108 | 22-108 | 22-108 | 
56 | Contractor | 1 | 22-109 | 22-109 | 22-109 | 
57 | Emergency stop | 1 | 22-099 | 22-099 | 22-099 | 
58 | Transit ring | 1 | 33-042 | 33-042 | 33-042 | 

## Slide 11
Item | Description | Qty | Part no. |  |  | Remark
 |  |  | HRM-30 | HRM-50 | HRM-60 | 
59 | Fuse holder | 1 | 22-101 | 22-101 | 22-101 | 
61 | Gear box | 1 | 33-034 | 33-034 | 33-034 | 
63 | Back cover | 1 | 33-010 | 33-010 | 33-010 | 
64 | Transformer | 1 | 22-107 | 22-107 | 22-107 | 
65 | Main Switch | 1 | 22-169 | 22-169 | 22-169 | 
66 | Electrical panel | 1 | 22-097 | 22-097 | 22-097 | 
67 | Start Switch | 1 | 22-100 | 22-100 | 22-100 | 
68 | Timer | 1 | 22-103 | 22-103 | 22-103 | 
69 | Chain | 1 | 33-028 | 42-007 | 53-005 | 
70 | Chain wheel 29 | 1 | 33-032 | 33-032 | 33-032 | 
71 | Bearing Connector | 1 | 33-019 | 33-019 | 33-019 | 
72 | Washer | 12 | 22-083 | 22-083 | 22-083 | 
73 | Spring washer | 8 | 22-089 | 22-089 | 22-089 | 
75 | Connector axle | 1 | 33-016 | 33-016 | 33-016 | 
77 | Connector key | 1 | 22-024 | 22-024 | 22-024 | 
78 | Engager | 1 | 33-020 | 33-020 | 33-020 | 
80 | Round bearing support | 1 | 33-035 | 33-035 | 33-035 | 
81 | Wheel 16 | 1 | 33-030 | 33-030 | 33-030 | 
83 | Transmission axles | 1 | 33-015 | 33-015 | 33-015 | 
98 | Lever | 1 | 22-072 | 22-072 | 22-072 | 
100 | Hook divider | 1 | 22-185 | 22-185 | 22-185 | 
101 | Hook | 1 | 22-161 | 22-161 | 22-161 | 
103 | Water shield | 1 | 33-061 | 33-062 | 33-063 | 
104 | Adjusting screw | 1 | 22-192 | 22-192 | 22-192 | 
105 | Auxiliary relay PCB | 1 | 22-281 | 22-281 | 22-281 | 
106 | Hook washer |  | 22-193 | 22-193 | 22-193 | 
110 | Electrical complete | 1 | 110-TR | 110-TR | 110-TR | 
111 | Spiral support complete | 1 | 111-TR33/42/53 | 111-TR33/42/53 | 111-TR33/42/53 | 
llustration Part list
Continue………

## Slide 12
End of user manual
Trouble | Cause | Solution
The machine does not start | Lack of electric energy in the power supply The Emergency stop switch is locked The safety guard and/or the head are up The knob of the general switch is in position “0” The timer is in position “0” | Check the main switch, the plug, the wire. Rotate the button following the direction of the arrow. Close correctly both the safety guard and the head. Rotate the knob in position 1 Rotate the knob of the timer form 1 to 30 minutes
The hook turns inconstantly | The chain is loose | Stretch the chain following the instructions as 5.2
The dough barrel makes a loud noise | 1. The dough hook touches the bottom of the dough bucket; 2. The dough hook touches the upper cover; 3. Severe friction between the dough mixer shaft and the chain | 1. Remove the upper cover, adjust the screws of the hook, and check the friction part; 2. Adjust the progress or length of the chain to see if it is longer or shorter.
The dough barrel cannot be removed | Long-term non-use, rusted and fixed; | Need to use it frequently or occasionally start it;
The dough mask does not stop even when it is pulled into place, or does not work when it is not pulled up | The dough mixer start contact piece deviates | Remove the upper cover of the machine and push the contact piece to the appropriate position
The barrel runs in the opposite direction to the direction indicated by the arrow | Plug wiring error | Stop the machine, take out the 2-phase line, and change the position of the two-phase plug (for example: swap L1 and L2, and vice versa)
Trouble shooting